Model: LulzBot Mini 2.0 3D Printer

  Serial Number:
  Date Completed:
  Tested by:

Configuration:
Electronics:	Einsy

Firmware:	Marlin Version

Nozzle:	0.5mm diameter nozzle
Settings:

Stepper Motor	Steps/mm	Max Length	Microstep Mode	Digipot
X	100.5	155	16	175
Y	100.5	155	16	175
Z	1600	165	16	220
E0	420	NA	16	135

Z Offset

General:
- Are all the screws and zip ties tight?
- Are the current version of parts being used?
- Is the Spool Mount properly mounted so it flips up and sits securely?
- Are the switches and bump stops installed securely?
- Are all 4 rubber feet installed?
- Is the PEI sheet free of bubbles and wrinkles?
- Is the heat bed adhesive smooth and consistent?
- Is the frame free of scratches and scuffs?

Y Axis:
- Does the Y bed move freely back and forth?
- Is the Y bed tight side to side from motion and twisting?
- Does the Y belt rub on the y-idler by the bearings?
- Are the Y pulley set screws tight with one aligned with the flat on the motor shaft?
- Is the Y belt tight?
- Are the four bed leveling washers tight?
- Are the belts trimmed far enough to not interfere with the pulley or bearing?

X Axis:

- Are the X pulley set screws tight with one aligned with the flat on the motor shaft?
- Does the X belt rub on the x-idler by the bearings?
- Is the X belt tight?
- Does the X axis move freely end to end?
- Are the belts trimmed far enough to not interfere with the pulley or bearing?
- Are the wires and zip ties behind the carriage free from touching the case wall?

Z Axis:

- Are the Z belts tensioned with in Spec?
- Are the clamp screws tight?
- Are the belts aligned, and do they not rub?
- Are the pulley set screws tight?
Extruder:

- Is the Idler tension set in the middle?
- Is the hobbing aligned to the hole idler lever?

Electronics:

- Are all connections to the Einsy plugged in correctly?
- Are all cables free from contacting any moving parts?
- Has the protective plastic been removed the LCD?
- Has the protective cover been removed from the clear polycarb LCD cover?
- Is the LCD secured in place firmly?
- Is the LCD knob tightly secure to the LCD?
- Have you verified that the firmware is correct using checksum?

Test and Verification Results:

- Verify LCD functions normally
- Belts aligned on bearings and properly tensioned.
- Verify case fan is running.
- Verify heat sink fan is running when machine is powered on.
- Verify control of the extrusion fan.
- Nozzle temperature control verified.
- Extruder control verified.
- Verify machine can be auto-homed repeatably with out issue.
- Verify probe functions properly (G29 and clean nozzle to check)
- Wipe Sequence is in center of wipe pad
- Z offset calibrated and verified
- Bed leveling is functioning properly.
- Bed temperature control verified.
- X,Y, Z motion smooth over range and speeds.
- Loctite® applied to all pulley and coupler set screws.
- Test print (Octopus*) successful.
- Print head moved to shipping position.

*Octopus by yeoldbrian is licensed under CC BY-SA 4.0